## Slide 1: Plans for R&D Report & Review
Objective
Develop GEM detectors for EIC forward tracker
Planned R&D activities June – Dec 2014
  Finish analysis of 2013 FNAL test beam data & write a NIM paper
  Measure gain uniformity of 1m zigzag detector with x-rays at Fl. Tech
  Address committee’s concern on long-term mechanical stability of stretched GEM foils by remeasuring gain performance of 1m prototype regularly, e.g. every month
  Test 10x10 zigzag detectors in magnetic field with table-top magnet since no magnet was available at FNAL test beam
  Collaborate with U. Va. and Temple U. on design of actual EIC forward tracker GEM segment for ~0.1m < r < ~1m
    note: GEM tested at FNAL was CMS design for ~1.5m < r < ~2.5m
    FIT to focus on latest spacer-less construction technique & zigzag strip readout
    U.Va.: low-mass readouts; Temple: GEM foil design
  Further help develop domestic commercial source of 1m-class GEM foils with TechEtch & Yale & Temple & CERN
Planned request for support
  Fully loaded FY2015 salary for Aiwu
  Small operations funds; few $k for gas, materials, travel

## Slide 2: Outlook beyond Dec 2014
If we want to build a large GEM tracker for EIC, we will need a domestic source of large GEM foils, i.e. TechEtch. CERN will be very busy with GEM production for LHC experiments.
TechEtch will need to make a substantial investment into new etching facilities for 1m-class foils including some initial non-recurring engineering (NRE) cost of probably a few 100k$.
Suggest to request significant financial support from EIC R&D for TechEtch to develop large-GEM production facilities. Suggest to propose first actual funding for TechEtch at Jan 2015 review/proposal meeting.
Once the prototype is designed, we should build a few chambers using exclusively domestic materials and put them into another test beam; maybe in fall 2015 ?